## Slide 1: Schema on the pipeline of Melomind
Fanny GROSSELIN
01-02-2017
Notes: 20/30s

## Slide 2: During Calibration

## Slide 3: During Calibration
This is rawCalibrationData which is used in the next pipelines.
initCalibrationData is sent to the server with the qualityCalibration on a Json file. initCalibrationData is without any process in order to have the original data for a possible work offline.
Add the 1s data on a matrix initCalibrationData for JsonFile
Replace bad quality data of rawCalibrationData by NaN values(1s by 1s)
(+ Correct artifacts online (for the future))
Raw data sent on the smartphone 1s by 1s
Linear interpolation of possible missing values
(1s by 1s)
DC removal
(1s by 1s)
+
Remove the powerline noise (notch at 50 and 100Hz) (1s by 1s)
Quality Checker
(1s by 1s)
1s
1s
1s
Add the quality data on a matrix qualityCalibration which holds one quality value by second for the JsonFile
Add the 1s interpolated data on a matrix rawSessionData.
rawSessionData can have NaN values if the quality is bad.
Add NULL in qualityCalibration which holds one quality value by second for the JsonFile
We don’t receive anything (packet lost)
yes
no

## Slide 4: At the end of the Calibration

## Slide 5: At the end of the Calibration
Keep it in memory to compute relaxation SNR from this channel during session
No need in the futur because we will correct artefacts online
rawCalibrationData of the best channel
without Bad data
Smooth SNR
4s by 4s with sliding window of 1s
Whole rawCalibrationData
DC removal (whole signal)
+
Remove the powerline noise (notch at 50 and 100Hz) (whole signal)
+
Apply a bandpass between 2 and 30Hz
Whole rawCalibrationData
Set the thresholds for the outliers
Keep them in memory for the session
DC removal
(whole signal)
+
Remove the powerline noise (notch at 50 and 100Hz) (whole signal)
+
Apply a bandpass between 2 and 30Hz
+
Apply a linear interpolation of the outliers based on the data of the whole signal from calibration
4s by 4s with sliding window of 1s
Compute SNR
4s by 4s with sliding window of 1s
Store it a SNRCalib vector
Keep them in memory (SmoothedSNRCalib) to normalize smoothed SNR from the session
qualityCalibration matrix
1s by 1s
Keep for each channel the packets with quality >= 0,5
each channel
Compute the average quality for each channel (only with the kept packets)
The best channel is the channel with the best quality (or the first one if the qualities are equal) and we can compute the SNR from calibration
best quality = 0,5
oui
non
Best channel = -2
Smoothed SNR from calibration = Inf values
Bad calibration
No need in the futur because we will correct artefacts online
+ trend correction 1/f

## Slide 6: During Session

## Slide 7: During Session
Add the 1s data on a matrix initSessionData for JsonFile
Replace bad quality data of rawSessionData by NaN values(1s by 1s)
(+ Correct artifacts online (for the future))
Raw data sent on the smartphone 1s by 1s
Linear interpolation of possible missing values
(1s by 1s)
DC removal
(1s by 1s)
+
Remove the powerline noise (notch at 50 and 100Hz) (1s by 1s)
Quality Checker
(1s by 1s)
1s
1s
1s
Add the 1s interpolated data on a matrix rawSessionData.
rawSessionData can have NaN values if the quality is bad.
Add the quality data on a matrix qualitySession which holds one quality value by second for the JsonFile
Each second, fill in a buffer of 4s from the rawSessionData of the best channel (see calibration)
4s by 4s with sliding window of 1s
DC removal
(whole signal)
+
Remove the powerline noise (notch at 50 and 100Hz) (whole signal)
+
Appky a bandpass between 2 and 30Hz
+
Apply a linear interpolation of the outliers based on the data of the whole signal from calibration
Smooth SNR
4s by 4s with sliding window of 1s
Compute SNR
1 value by second
Store it a SNRSession vector
Normalize Smoothed SNR with mean and std of smoothed SNR from calibration
Transform into volum value
If normalized smoothed SNR value = NaN, volum = 0,5 or previous value
1 value by second
1 value by second
No need in the futur because we will correct artefacts online
Add NULL in qualityCalibration which holds one quality value by second for the JsonFile
We don’t receive anything (packet lost)
yes
no
1s
+ trend correction 1/f
volum = 0,5 or Previous value?

## Slide 8: During Session
This is rawSessionData which is used to compute the relaxation index and statistics about relaxation state. The NaN values correspond to bad quality values.
initSessionData is sent to the server with the qualitySession on a Json file. initSessionData is without any process in order to have the original data for a possible work offline.

## Slide 9: At the end of the Session

## Slide 10: At the end of the Session
Remove NaN (bad quality) values
No need in the futur because we will correct artefacts online
rawSessionData of the best channel
Whole rawSessionData
DC removal (whole signal)
+
Remove the powerline noise (notch at 50 and 100Hz) (whole signal)
+
Apply a bandpass between 2 and 30Hz
Whole rawSessionData
Set the thresholds for the outliers
Apply a linear interpolation of the outliers based on the data of the whole preprocessed rawSessionData
Some statistics are computed on the whole EEG signal from the session. These statistics concern the relaxation state.
Trend correction 1/f