## Slide 1: Schema on the pipeline of Melomind
Fanny GROSSELIN
06-02-2017
Notes: 20/30s

## Slide 2: During Calibration

## Slide 3: During Calibration
Add the 1s data on a matrix initCalibrationData for JsonFile
Replace bad quality data of rawCalibrationData by NaN values(1s by 1s)
(+ Correct artifacts online (for the future))
Raw data sent on the smartphone 1s by 1s
Linear interpolation of possible missing values
(1s by 1s)
DC removal
(1s by 1s)
+
Remove the powerline noise (notch at 50 and 100Hz) (1s by 1s)
Quality Checker
(1s by 1s)
1s
1s
1s
Add the quality data on a matrix qualityCalibration which holds one quality value by second for the JsonFile
Add the 1s interpolated data on a matrix rawCalibrationData.
rawCalibrationData can have NaN values if the quality is bad.
Add 0 in qualityCalibration which holds one quality value by second for the JsonFile
We don’t receive anything (packet lost)
yes
no
Add 250 data points with NaN values in rawCalibrationData
(If we don’t do that there will be a time lag in rawCalibrationData and SNR will not be computed on 4 consecutive seconds)

## Slide 4: During Calibration
What is keep in memory in the smartphone?
This is rawCalibrationData (array of 2 rows) which is used in the next pipelines  keep it in memory of the smartphone until the end of the processes which are done at the end of calibration.

## Slide 5: At the end of the Calibration

## Slide 6: At the end of the Calibration
Keep it in memory to compute relaxation SNR from this channel during session
No need in the futur because we will correct artefacts online
rawCalibrationData of the best channel
without Bad data
Smooth SNR
Whole rawCalibrationData
without NaN values
DC removal (whole signal)
+
Remove the powerline noise (notch at 50 and 100Hz) (whole signal)
+
Apply a bandpass between 2 and 30Hz
Whole rawCalibrationData
without NaN values
Set the thresholds for the outliers
Keep them in memory for the session
DC removal
(whole signal)
+
Remove the powerline noise (notch at 50 and 100Hz) (whole signal)
+
Apply a bandpass between 2 and 30Hz
+
Apply a linear interpolation of the outliers based on the data of the whole signal from calibration
4s by 4s with sliding window of 1s without NaN values
Compute SNR
4s by 4s with sliding window of 1s without NaN values
Store it in a SNRCalib vector to be able to smooth with the previous SNR values
Keep them in memory (SmoothedSNRCalib) to normalize smoothed SNR from the session
qualityCalibration matrix
1s by 1s
Keep for each channel the packets with quality >= 0,5
each channel
Compute the average quality for each channel (only with the kept packets)
The best channel is the channel with the best quality (or the first one if the qualities are equal) and we can compute the SNR from calibration
best quality < 0,5
(It’s possible because it is initialized at 0)
oui
non
Best channel = -2
Smoothed SNR from calibration = Inf values
Bad calibration
No need in the future because we will correct artefacts online
+ trend correction 1/f
Remove NaN values (bad quality or no received data)
Whole rawCalibrationData
Remove NaN values (bad quality or no received data)
4s by 4s with sliding window of 1s without NaN values

## Slide 7: At the end of the Calibration
What we sent to the server ?
initCalibrationData is sent to the server with the qualityCalibration on a Json file. initCalibrationData is without any process in order to have the original data for a possible work offline.
What is keep in memory in the smartphone?
The best channel (with the best quality) (int = 0 or 1) and a vector which holds all the Smoothed SNR values from the calibration (vector of float)  keep it in memory of the smartphone until the end of the processes which are done at the end of session. We have also to keep in memory the bounds of the outliers (vector of 2 floats).
What is remove from memory of the smartphone?
rawCalibrationData

## Slide 8: During Session

## Slide 9: During Session
Add the 1s data on a matrix initSessionData for JsonFile
Replace bad quality data of rawSessionData by NaN values(1s by 1s)
(+ Correct artifacts online (for the future))
Raw data sent on the smartphone 1s by 1s
Linear interpolation of possible missing values
(1s by 1s)
DC removal
(1s by 1s)
+
Remove the powerline noise (notch at 50 and 100Hz) (1s by 1s)
Quality Checker
(1s by 1s)
1s
1s
1s
Add the 1s interpolated data on a matrix rawSessionData.
rawSessionData can have NaN values if the quality is bad.
Add the quality data on a matrix qualitySession which holds one quality value by second for the JsonFile
Each second, fill in a buffer of 4s from the rawSessionData of the best channel (see calibration)
DC removal
(whole signal)
+
Remove the powerline noise (notch at 50 and 100Hz) (whole signal)
+
Apply a bandpass between 2 and 30Hz
+
Apply a linear interpolation of the outliers based on the data of the whole signal from calibration
Smooth SNR
4s by 4s with sliding window of 1s
without NaN values
Compute SNR
1 value by second
Store it in a SNRSession vector to be able to smooth with the previous SNR values
Normalize Smoothed SNR with mean and std of smoothed SNR from calibration
Transform into volum value
If normalized smoothed SNR value = NaN, volum = 0,5 or previous value
1 value by second
1 value by second
No need in the futur because we will correct artefacts online
We don’t receive anything (packet lost)
no
1s
+ trend correction 1/f
Add 0 in qualitySession which holds one quality value by second for the JsonFile
Add 250 data points with NaN values in rawSessionData (If we don’t do that there will be a time lag in rawSessionData and SNR will not be computed on 4 consecutive seconds)
yes
4s by 4s with sliding window of 1s
Remove NaN values (bad quality or no received data)
4s by 4s with sliding window of 1s without NaN values

## Slide 10: During Session
What is keep in memory in the smartphone?
- This is rawSessionData (array of 1 row of float) which is used to compute the relaxation index and statistics about relaxation state. The NaN values correspond to bad quality values or data no received  keep it in memory of the smartphone until the end of the processes which are done at the end of session.
- Keep also in memory the normalized smoothed SNR values from the session to draw some plots at the end of the session.

## Slide 11: At the end of the Session

## Slide 12: At the end of the Session
Remove NaN (bad quality or not received data) values
No need in the futur because we will correct artefacts online
rawSessionData of the best channel
Whole rawSessionData
without NaN values
DC removal (whole signal)
+
Remove the powerline noise (notch at 50 and 100Hz) (whole signal)
+
Apply a bandpass between 2 and 30Hz
Whole rawSessionData
without NaN values
Set the thresholds for the outliers
Apply a linear interpolation of the outliers based on the data of the whole preprocessed rawSessionData
Some statistics are computed on the whole EEG signal from the session. These statistics concern the relaxation state.
Trend correction 1/f

## Slide 13: At the end of the Session
What we sent to the server ?
- initSessionData is sent to the server with the qualitySession on a Json file. initSessionData is without any process in order to have the original data for a possible work offline.
- Statistics.
What is keep in memory in the smartphone?
Nothing.
What is remove from memory of the smartphone?
rawSessionData